## Slide 1: Energi Terbarukan
Dosen Pengampu:
Frida Hasana, S.Pd. M.Eng.
Pertemuan 2:
Solar PV

## Slide 2: Solar PV
Modified from:
Master of Electrical Engineering – UGM
Ir. Lesnanto Multa Putranto, S.T., M.Eng., Ph.D., IPM., SMIEEE.

## Slide 3: Solar Domestic Hot Water

## Slide 4: Solar PV System On Grid
Solar PV rooftop
Solar PV farm

## Slide 5
Gonghe Talatan Solar Park stands as the undisputed champion of solar installations worldwide. The site spreads over 609 km² (almost equivalent to Singapore’s land area). This massive complex, located in China’s Qinghai Province, has been developed in multiple phases since 2011, with continuous expansion pushing its capacity to an astounding 15.6 GW. The facility includes over 7.2 million solar panels and incorporates various panel designs for testing and optimization purposes.

## Slide 6
The largest solar power plant in Indonesia is currently the Cirata Floating Solar Plant in Purwakarta, West Java. It has an installed capacity of 192 MWp, occupying about 250 hectares over the Cirata Reservoir, and is capable of powering over 50,000 households annually. Developed through a collaboration involving PLN and Masdar, it is also Southeast Asia’s largest floating solar plant.
(The Jakarta Post)

## Slide 7: Global Mean Solar Irradiance

## Slide 8: Photovoltaic (PV) Hierarchy
Cell < Module < Panel < Array

## Slide 9: Inside of PV Cell
Solar cells consist of two layers of semiconductor material with opposite charges. Sunlight hitting the surface of a cell causes electrons to be knocked loose, which then travel through a circuit from one layer to the other, generating a flow of electricity.

## Slide 10
PV SYSTEMS TECHNOLOGIES

## Slide 11: PV Systems Technology
1st Generation
The manufacturing process of wafer-based silicon PV modules comprises four steps:
Polysilicon production;
Polysilicon production;
Ingot/wafer production;
Cell production; and
Module assembly.
Crystalline silicon cells are classified into three main types depending on how the Si wafers are made :
  Monocrystalline (Mono c-Si), sometimes also called single crystalline (sc-Si)
  Polycrystalline (Poly c-Si), sometimes referred to as multi-crystalline (mc-Si)
  EFG ribbon silicon and silicon sheet-defined film growth (EFG ribbon-sheet c-Si)

## Slide 12
Monocrystalline Modules
Most efficient commercially available module (11% - 14%)
Most expensive to produce
Circular (square-round) cell creates wasted space on module.
Polycrystalline Silicon Modules
Less expensive to produce than single crystalline modules.
Cells are slightly less efficient than single crystalline ones (10% - 12%).
Square-shaped cells fit into the module efficiently, using the entire space.
1st Generation

## Slide 13: PV Systems Technology
2nd Generation: Thin Film
Require a lot less semiconductor material to manufacture in order to absorb the same amount of sunlight (up to 99% less material than crystalline solar cells).
Thin films can be packaged into flexible and lightweight structures, which can be easily integrated into building components.
The three primary types of thin-film solar cells that have been commercially developed are:
  Amorphous silicon (a-Si and a-Si/μc-Si);
  Cadmium Telluride (Cd-Te); and
  Copper-Indium-Selenide (CIS) and Copper-Indium-Gallium-Diselenide (CIGS).

## Slide 14
2nd Generation: Thin Film
Amorphous Thin Film
Most inexpensive technology to produce
Metal grid replaced with transparent oxides
Efficiency = 6 – 8 %
Can be deposited on flexible substrates
Less susceptible to shading problems
Better performance in low light conditions that with crystalline modules

## Slide 15: PV Systems Technology
3rd Generation
There are four types of third-generation PV technologies:
Concentrating PV (CPV);
  Utilise optical devices, such as lenses or mirrors, to concentrate direct solar radiation onto very small, highly efficient multi-junction solar cells made of a semiconductor material.
  The sunlight concentration factor ranges from 2 to 100 suns (low-to medium-concentration) up to 1000 suns (high concentration).
Dye-sensitized solar cells (DSSC);
  Use photo-electrochemical solar cells, which are based on semiconductor structures formed between a photo-sensitised anode and an electrolyte.
  Use low-cost materials and are simple to manufacture.
Organic solar cells;
  composed of organic or polymer materials (such as organic polymers or
small organic molecules); inexpensive but not efficient
Novel and emerging solar cell concepts.

## Slide 16: Selecting the Correct Module
Practical Criteria
  Size
  Voltage
  Availability
  Warranty
  Mounting Characteristics
  Cost (per watt)

## Slide 17: Current Voltage (I-V) Curve

## Slide 18: Current Voltage (I-V) Curve
Isc (Short Circuit Current)
  The point where voltage= 0 (short circuit)
Voc (Open Circuit Voltage)
  The point where current = 0 (open circuit)
Pmax (Maximum Power)
  Pmax​ = Vmp ​× Imp​
MPPT (Maximum Power Point Tracking)
  Optimizes and stabilizes the system to always operate at Vmp and Imp

## Slide 19: Effect of Temperature
As the PV cell temperature increases above 250C, the module Vmp decreases by approximately 0.5% per 0C
PV cell produces power supplied by irradiance, not by temperature

## Slide 20: Effect of Shading/Low Insolation
As insolation increases, amperage increases while voltage remains roughly constant

## Slide 21
PV WIRING

## Slide 22: Solar PV System On Grid

## Slide 23
PV WIRING
VOLTAGES ARE ADDITIVE
CURRENT IS EQUAL
VOLTAGE REMAINS CONSTANT
CURRENTS ARE ADDITIVE
Loads/sources wired in parallel
Loads/sources wired in series

## Slide 24
PV ANGEL
&
MOUNTING

## Slide 25: Solar Energy Source
Understand azimuth and altitude
Describe the proper orientation and tilt angle for solar collection
Describe the concept of “solar window”
Evaluate structural considerations
Pros and cons of different mounting techniques

## Slide 26
Optimum Solar Window 9 am – 3 pm
Max performance is achieved when panels are perpendicular to the sun’s rays
Array should have NO SHADING in this window (or longer if possible)
Solar Access
Altitude (sun elevation)
Azimuth (sun direction)
Tilt (solar panel tilt)
Panel Direction

## Slide 27: Basic Mounting
FIXED
Roof
Ground
Pole
INTEGRATED
TRACKING
Pole Active
Pole Pasive

## Slide 28: END